| NAT: NATURAL RESOURCES |
| --- |
| Forestry |
| task | Using Safety Ropes |
| hazards | Potential Hazards | Possible Consequences |
| Physical | lifting and handling loads repetitive motion slips, trips, and falls | musculoskeletal injuries contusions abrasions |
| Chemical | n/a | n/a |
| Biological | bacteria/viruses blood body fluids | illness |
| Ergonomic | poor or awkward posture repetitive movement muscular strength and endurance | musculoskeletal injuries |
| Psychological | fatigue stress | inattentiveness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. For example, regularly check for flaws along the entire length of the rope and replace as needed. Inspect PPE and replace if required. Report any hazards. |
| Safe Work Procedure | Cautions |
| Put on required PPE. Wear proper footwear. Secure loose clothing, and tie back long hair. Remove jewellery. Use tools and equipment under competent supervision. Read and follow the manufacturer’s instructions. Follow the school safety policy. Put away all tools, equipment, and materials in their proper storage areas. Ropes should be kept coiled when not in use and stored in ventilated boxes. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | Move ropes slowly over limbs or between the legs to prevent friction damage.* Never use safety lines for raising and lowering equipment or tree limbs.* |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |

Content throughout this document that is identified with * was provided by: Landscaping, Tree Trimming. http://www.ccohs.ca/oshanswers/safety_haz/landscaping/tree_trimming.html OSH Answers, Canadian Centre of Occupational Health and Safety (CCOHS), 2008. Reproduced/Adapted with the permission of CCOHS, 2013