| NAT: NATURAL RESOURCES |
| --- |
| Wildlife |
| task | Using a Gas Auger |
| hazards | Potential Hazards | Possible Consequences |
| Physical | lifting and handling loads repetitive motion slips, trips, and falls moving parts vibration sharp blade | musculoskeletal injuries contusions lacerations abrasions pinching puncture wounds |
| Chemical | cleaning agent, oil, gasoline | chemical burns skin irritation lung damage headache dizziness loss of consciousness |
| Biological | bacteria/viruses blood body fluids | illness |
| Ergonomic | incorrectly set height of auger poor or awkward posture repetitive motion lack of muscular strength, endurance, flexibility, and/or balance vibration incorrect handle height for user | bodily injury |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. Inspect PPE and replace if required. Report any hazards. Clean the air intake, air filter, and spark plugs. Read, understand, and follow the manufacturer's operating manual and safety decals on the equipment before operating the equipment. (Go to www.ccohs.ca for more information.) Inspect and tighten blade screws and all joints. Check the gas to oil ratio. |
| Safe Work Procedure | Cautions |
| Put on all required PPE. Wear non-slip shoes. Secure loose clothing. Remove jewellery. Read and follow the manufacturer’s instructions, precautions, and directions. Follow specific manufacturer instructions for priming and starting the unit with careful attention to safety recommendations. Follow the school safety policy. Set the height of auger. Uncover the blade. When cold starting, let the engine warm up for a few minutes. Set the blade on the ice. Once finished, shake the ice from the blade. Put away all tools, equipment, and materials in their proper storage areas. Clean the work area. Establish handwashing practices. | Keep the blade sharpened. Properly secure the auger for transport. Transport the auger with the gas cap on the vent screw closed. Always cover the blade when not in use. Stay warm and keep focused on the task at hand. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |