| TMT: TRADES, MANUFACTURING, and TRANSPORTATION |
| --- |
| Construction |
| task | Using a Band Saw |
| hazards | Potential Hazards | Possible Consequences |
| Physical | flying objects electrical shock lifting and handling loads noise repetitive motion moving parts sharp blade | bruising pinching cuts/amputations hearing loss eye irritation and/or eye damage repetitive motion injury |
| Chemical | wood dust human-made material particulates (e.g., lexan, polycarbonate, laminates, MDF, and plywood) | respiratory damage |
| Biological | bacteria/virus blood body fluids | illness |
| Ergonomic | lifting heavy stock materials vibration lighting | bodily injury eye strain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect the tools, equipment, and materials for damage and other hazards. For example, check for electrical cord and switch damage. Inspect the material for knots, splits, warp, nails, staples, or other defects. Inspect PPE and replace if required. Report any hazards. Check that all guards are in place and working correctly. |

| Safe Work Procedure | Cautions |
| --- | --- |
| Put on required PPE. Secure loose clothing, and tie back long hair. Follow the manufacturer’s instructions. Follow the school safety policy. Position the material on the machine table. Adjust the blade guard/guide to ¼ in above the material. Turn on the machine. Feed the material into the blade and complete the cut, maintaining a 5-cm or 2-in margin of safety. Use a push stick if necessary. Feed the stock at a steady controlled pace, no faster than the blade can easily cut. Hold the stock flat on the table. Turn the machine off, and wait for the blade to completely stop. Remove the material from the band saw table. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | Do not breathe in vapours or dust. Use a stable and comfortable stance. Never put your fingers in line with the blade. Focus your attention on the point of the cut (where the blade enters the wood). If you hear a clicking noise (indicating a broken blade), turn the machine off and move your hands away from blade until the machine stops. Use relief cuts for cutting curves. Turn the machine off before backing out of a cut. Use a V-block for cutting round stock, such as dowels. Feed the stock at a steady controlled pace, no faster than the blade can easily cut. Hold the stock flat on the table |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |