| TMT: TRADES, MANUFACTURING, and TRANSPORTATION |
| --- |
| Construction |
| task | Using Lumber |
| hazards | Potential Hazards | Possible Consequences |
| Physical | lifting and handling loads | bruising pinching |
| Chemical | wood dust | respiratory illness eye irritation |
| Biological | n/a | n/a |
| Ergonomic | lifting and moving heavy materials | bodily injury |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Refer to the MSDS for wood dust. Inspect tools, equipment, and materials for damage and other hazards. Inspect PPE and replace if required. Report any hazards. |
| Safe Work Procedure | Cautions |
| Put on required PPE. Follow the school safety policy. Refer to the safe work procedure for the tool or equipment to be used and the specific operation. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. | When lifting lumber, use your leg and arm muscles (not your back muscles) and seek assistance when the weight is unreasonable for one person. Keep lumber stacked and stored neatly so that it does not project into shop pathways. Use a cart or trolley for transporting heavy lumber. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |