| Task hazard analysis |
| --- |
| Electro-Technologies |
| task | Using a Milliammeter/Ammeter |
| hazards | Potential Hazards | Possible Consequences |
| Physical | electrical | electrical shock burns |
| Chemical | n/a | n/a |
| Biological | bacteria/viruses blood body fluids | Where others have touched devices, possible contamination via viruses/bacteria may occur. |
| Ergonomic | n/a | n/a |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and hazards. For example, check the meter leads. Report any hazards. |

| Safe Work Procedure | Cautions |
| --- | --- |
| Use tools and equipment under competent supervision. Follow the manufacturer’s instructions. Follow the school safety policy. Place leads in the correct jacks: red is positive and black is negative. There is no polarity when measuring AC, but polarity must be observed when measuring DC. De-energize the circuit to be tested. Connect the milliammeter/ammeter in series with the load. This means the circuit under test must be opened (taken apart). Unless the milliammeter/ammeter is auto-ranging, the ranges are finite. Start on the highest range and work down. The maximum rating of the milliammeter/ammeter for any range must not be exceeded. Have the work inspected by the instructor before energizing. Energize the circuit and observe the digital read-out or the reading from the appropriate scale if the milliammeter/ammeter is analog. De-energize the circuit and disconnect the milliammeter/ammeter. Restore the circuit under test. Put away all tools, equipment, and materials in their proper storage areas. Clean the work area. Establish handwashing practices. | Make sure the circuit to be tested is de-energized before attempting to open the circuit to make connections. Make sure the milliammeter/ammeter is connected in series with the load. This means the circuit under test must be opened (taken apart). The maximum rating of the milliammeter/ammeter for any range must not be exceeded. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |