| Task hazard analysis |
| --- |
| Electro-Technologies |
| task | Using an Ohmmeter |
| hazards | Potential Hazards | Possible Consequences |
| Physical | electrical | electrical shock burns |
| Chemical | n/a | n/a |
| Biological | bacteria/viruses blood body fluids | Where others have touched devices, possible contamination via viruses/bacteria may occur. |
| Ergonomic | n/a | n/a |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. For example, inspect meter leads. Report any hazards. |
| Safe Work Procedure | Cautions |
| Use tools and equipment under competent supervision. Follow the manufacturer’s instructions. Follow the school safety policy. Place leads in the correct jacks: red is positive and black is negative. If the ohmmeter is analog, “zero” the meter. Ensure the component to be tested is de-energized. Connect the ohmmeter across (in parallel with) the component to be tested. Unless the ohmmeter is auto-ranging, select the range that will give the most accurate reading. Observe the digital read-out or the reading from the appropriate scale if the ohmmeter is analog. Disconnect the ohmmeter and switch off. Put away all tools, equipment, and materials in their proper storage areas. Clean the work area. Establish handwashing practices. | Make sure the component to be tested is de-energized before attempting to connect the ohmmeter. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |