| CLUSTER | TMT: TRADES, MANUFACTURING, AND TRANSPORTATION |
| --- | --- |
| OCCUPATION | Fabrication |
| HAZARD CONTROLS | EQUIPMENT—DRILL PRESS (DRY OR WET) |
| Engineering Controls | Adapted from iStockphoto/Thinkstock |
| ventilation system dust and fume extraction equipment pulley enclosure magnetic motor starter switch use of proper bit size and type for specific operation equipment securely fastened in place |  |
| Administrative Controls |  |
| Provide initial training to include a thorough review of hazards and accidents associated with the job. Follow the school safety policy. Provide and document ongoing safety education and training, including mandatory equipment and tool orientation. Outline the “imminent danger/right to refuse” procedures. Ensure hazard signs and tags are in place. Tag and remove defective equipment from service. Ensure equipment is used under competent supervision. Ensure the equipment is appropriate for the work to be done. Schedule work to avoid overcrowding. Ensure repetitive tasks are properly paced. Post important emergency telephone numbers and contacts. Post lockdown procedures. Post fire drill procedures. Establish handwashing practices. Locate the emergency electrical shut-off. Provide safe clearance for the equipment. Place a non-slip surface on the floor. Mark lines on the floor to designate the work space. Ensure fire extinguishers are strategically located and marked. Provide a first aid kit and supplies, including an eyewash station and biohazard disposal. Ensure that the master control panel and panel breakers are properly labelled. Keep the manufacturer’s manual for the equipment. Provide an ergonomically appropriate work area. Ensure that correct lighting is available. Correctly place and maintain smoke detectors and heat sensors. Post relevant safety and health facts in the work area. Ensure that students wear safe attire: no loose clothing or jewellery should be worn. Ensure that long hair is tied back and/or secured under a hat. Follow lock-out procedures for performing maintenance. Ensure WHMIS training is available. Provide up-to-date MSDS. Properly label controlled products. Secure and use the least toxic and harmful substance for the students and the environment. Adhere to OHS occupational exposure limits (OELs). Adhere to the Canadian Electrical Code during the operation, repair, and maintenance of equipment. Post “high-voltage” signage. Use a minimum 5-cm or 2-in margin of safety. Clamp material whenever possible, especially small pieces. Remove the chuck key from the chuck as soon as the bit change is complete. Use the speed settings recommended by the manufacturer. |  |
| Personal Protective Equipment (PPE) |  |
| safety glasses (CSA approved) coveralls steel-toed safety boots (CSA approved) |  |