| TMT: TRADES, MANUFACTURING, AND TRANSPORTATION |
| --- |
| Fabrication |
| task | Using an Angle Grinder (4½ in–7 in) |
| hazards | Potential Hazards | Possible Consequences |
| Physical | electrical shock eye hazards: chipping, grinding, flying metal or dirt fire and explosion lifting and handling loads excessive noise repetitive motion slips, trips, and falls hot parts moving parts confined spaces | death bruising pinching eye irritation and/or eye damage hearing impairment burns cuts chronic pain cancer repetitive motion injuries |
| Chemical | fumes: aluminum, beryllium, cadmium oxides, chromium, copper, fluorides, iron oxide, lead, manganese, molybdenum, nickel, vanadium, zinc oxides gases: carbon monoxide, hydrogen fluoride, nitrogen oxide, ozone, phosphine organic vapours: aldehydes (such as formaldehyde), di-isocyanates, phosgene compressed-gas cylinders: argon, carbon dioxide, acetylene, oxygen, MAPP, propane | Acute effects (occurring immediately or quickly) include metal fume fever; damage to the respiratory tract; sore and dry throat; chest pain; breathing difficulty; skin irritation; irritation of the eyes, nose, and throat; nausea; dermatitis; headache; dizziness; and muscular weakness. Chronic effects (appearing over time) include kidney damage; emphysema; cancer; bone and joint problems; excess fluid in the lungs; siderosis; chronic effects to the nervous system, kidneys, digestive system, and mental capacity; lead poisoning; bronchitis; retinitis; pneumonia; and asphyxiation. oxygen deficiency burns death |
| Biological | allergens: fumes and gases bacteria/viruses blood body fluids | asthma or other allergy symptoms illness |
| Ergonomic | work surface height lifting repetitive work | bodily injury chronic pain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. Report any hazards. Guards must be on grinders and adjusted for the user. Inspect PPE and replace if required. Adjust the work surface height appropriately for the user. Check that the ventilation system is operational before starting to grind. |
| Safe Work Procedure | Cautions |
| Put on required PPE. All grinding processes produce hazardous fumes. Minimize your exposure. Secure loose clothing, and do not wear worn or frayed clothing that may ignite. Tie back long hair. Use tools and equipment under competent supervision. Follow the manufacturer’s instructions. The person grinding is responsible for the spray of sparks. Work in isolation or behind a barrier to minimize exposure of others to flying particles when necessary. Make sure that there are no flammable products in or near the workspace. Follow the school safety policy. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | n/a |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |