| TMT: TRADES, MANUFACTURING, and TRANSPORTATION |
| --- |
| Fabrication |
| task | Using a Vertical Band Saw |
| hazards | Potential Hazards | Possible Consequences |
| Physical | electrical shock eye hazards: flying metal or dirt fire and explosion lifting and handling loads excessive noise repetitive motion hot parts tools and machinery moving parts | death bruising pinching eye irritation and/or eye damage hearing impairment burns cuts repetitive motion injuries chronic pain |
| Chemical | n/a | n/a |
| Biological | bacteria/viruses blood body fluids | illness |
| Ergonomic | work surface height lifting repetitive work | bodily injury chronic pain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. Inspect PPE and replace if required. Report any hazards. Adjust the work surface height appropriately for the user. |

| Safe Work Procedure | Cautions |
| --- | --- |
| Put on required PPE. Secure loose clothing, and tie back long hair. Use tools and equipment under competent supervision. Follow the manufacturer’s instructions. Follow the school safety policy. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | n/a |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |